## Slide 1: Regional Air Quality Modeling
Daniel Tong
CLIM 670 Earth System Modeling (Prof. Pegion)
George Mason University
November 17, 2020

## Slide 2: Outline
1) Fundamentals of air quality;
2) Concepts of regional air quality modeling;
3) Typical applications;
4) CMAQ Lab Experiment: Wildfire Forecasting;

## Slide 4: Criteria Air Pollutants
Aerosols | 
PM2.5 | Particulate Matter smaller than 2.5 microns
PM10 | Particulate Matter smaller than 10 microns
Pb | Lead
Trace Gases | 
O3 | Ozone
NO2 | Nitrogen Dioxide
SO2 | Sulfur Dioxide
CO | Carbon Monoxide
(More reading: https://www.epa.gov/criteria-air-pollutants/naaqs-table)

## Slide 5: PM10 and PM2.5

## Slide 7: Some Facts about Air Pollution
Air Pollution is No. 1 environmental killer;
Kills more than 8 millions each year;
Over one third of Americans breathe unhealthy air;

## Slide 8
Chemistry of the Atmosphere
(Picture in the public domain)
Additional Courses at Mason:
CLIM319: Air Pollution
CLIM438: Atmospheric Chemistry
CLIM769-002: Aerosols

## Slide 9
Simple Eulerian Box Model
Inflow
Outflow
Emission
Deposition
Chemical Transformation

## Slide 10
Comprehensive Air Quality Models
(Source: EPA)
CMAQ – Community Multiscale Air Quality model

## Slide 11
Regional Air Quality Modeling
Air Quality Model
Meteorology Model
Emission Model

## Slide 12
Emission Modeling
Emission Inventories
Model-ready Emission
Real World Emissions

## Slide 13: GMU Air Quality Forecast Capability
Operated by GMU;
Provides national numerical air quality guidance for ozone and PM2.5 (particulate matter with diameter < 2.5 mm);
O3 Forecasting
PM2.5 Forecasting

## Slide 14: Application 1. Impact of the Social Events on US Air Quality
Great Depression
Starting – Ending time: December 2007 – October 2009;
Cause: Bursting of the housing bubble in 2007, followed by a subprime mortgage crisis in 2008;
Impacts:
  Unemployment rate: 4.7% in Nov 2007  10.1% in Oct 2009.
  Income level: dropped to 1996 level after inflation adjustment;
  Poverty rate: 12%  16% (50 millions);
  GDP: contract by 5.1%;
Worst economic recession since the Great Depression
Question: What does it mean to Air Quality (and Emissions)?

## Slide 15
Ozone Monitoring Instrument (OMI)
One of four sensors on the EOS-Aura platform (OMI, MLS, TES, HIRDLS)
Launched on 07-15-04
Courtesy of OMAR Torres
Data Quality Control
- VCD quality flag;
- Cloud fraction;
Row Anomaly;
Outliners (5% at each end)
Instrument Characteristics
-Nadir solar backscatter spectrometer
-Spectral range 270-500 nm (resolution~0.6 nm )
Spatial resolution: 13X24 km footprint
Swath width: 2600 km (global daily coverage)
13:45 (+/- 15 min) Local equator crossing time (ascending node)

## Slide 16
AQS: EPA Ambient NO2 Monitoring
Method: Chemiluminescence
  Interferences with PAN, O3 and alkyl nitrates
  Uncertainty higher at lower end
Select early morning rush hours (6-9AM): higher values and less photochemistry

## Slide 17: OMI Observed NOx Change (July)
Contributed by Lok Lamsal

## Slide 18: Inter-Comparison of OMI, AQS and NAQFC Model
Los Angeles
New York
Philadelphia
NOx Change from 2005 Level (%)
Washington, DC
(Source: Tong et al., 2015)

## Slide 19
Rapid Refresh of NOx Emissions
19
Question: Can satellite and ground data be used to rapidly refresh NOx emissions?
Fusing ground and satellite data:
State-level Adjustment Factors
(2005 to 2012)
(Source: Tong et al., GRL, 2016)
AF – Adjustment Factor
△S – Change in Satellite data;
△G – Change in Ground data;
NS – Satellite sample size;
NG – Ground sample size;
fS – Satellite weighing factor;
fG – Ground weighing factor;

## Slide 20
Business As Usual (2011-2005)
Recession (2011-2005)
O3 Changes Caused by Recession
Recession Impact on US Air Quality
(Source: Tong et al., GRL, 2016)
Quantifying Recession Impact:
  BAU: EPA Projection;
  Recession: Observed Changes;
  Difference: Recession impact.
Notes: We use this approach to quantify the impact of the 2008 Great Recession on the US air quality.
The Recession impact is estimated from the difference between two model simulations using the Business as Usual and the Economic Recession scenarios. IN the Business as Usual case, the EPA emission projection for the Cross-State Air Pollution Rule (CSAPR) is used to represent the “would-be” emission level without the recession. IN the recession case, the observed emission trends are used to represent the actual emissions changes.
In both cases, surface ozone concentration decreased from 2005 to 2011 as a results of reduced emissions. The difference between business as usual and recession, which is shown at the botthom, showed theRecession has reduced ozone further in the eastern US and the Pacific west. The ozone concentration increased in southern California, due to reduced titration by emitted NO. There was also an increase in central US, which is caused by increased emissions from the oil and gas operations in this region

## Slide 21: World Air Quality during COVID-19
(Source: European Space Agency)

## Slide 22: Post-COVID-19 Air Quality
Emissions in China returned and surpassed historic levels quickly after the lifting of lock-down.
Similar trends observed in the U.S. during the 2008 Recession (Tong et al., 2015)
(Source: European Space Agency)

## Slide 23
COVID-19 Impacts on U.S. Air Quality
Using emission changes based on satellite and ground data, we use the Community Multiscale Air Quality (CMAQ) model to quantify COVID-19 effects on U.S. air quality.
March 15-April 15, 2020
Ground-level ozone changes (%)
Oxides of nitrogen emission changes (%)
Increases
Increases
Decreases
Decreases
(Patrick Campbell, GMU/NOAA)

## Slide 24
Kilauea Volcanic Eruption - Hawaii
(Source: Earther)
Notes: NOTE: notes not added—please add to your slide.

## Slide 25
Sulfur Dioxide (SO2) Prediction of
the Kilauea Volcanic Eruption
25
Without Volcanic Emissions
With Volcanic Emissions
(Source: Tang et al., 2020)
Notes: NOTE: notes not added—please add to your slide.

## Slide 26: The “Dust Bowl”
Causes: Extended droughts and poor land management;
SD-1936
(Source: USDA)
Notes: Homestead Acts: settlement over the Plains for agriculture ;
“Rain follows the plow”: unusually wet climate;
New agricultural machinery: Deep plowing, eliminating native grass;
Favorable dust storm conditions during 1930s drought

## Slide 27: The “Dust Bowl”
Impacts:
Stripped 75% of top soils over thousands of farms;
Destroyed agriculture and ecosystem (~1950s);
> 500,000 lost homes and communities;
"And then the dispossessed were drawn west--from Kansas, Oklahoma, Texas, New Mexico; from Nevada and Arkansas, families, tribes, dusted out, tractored out... They streamed over the mountains, hungry and restless--restless as ants, scurrying to find work … anything, any burden to bear, for food. The kids are hungry. We got no place to live…”
-- John Steinbeck in the Grapes of Wrath

## Slide 28
Another “Dust Bowl”?
Central U.S. plains saw severe droughts about once or twice a century over the past 400 years (Woodhouse & Overpeck, 1998).
This recurring trend may be enhanced global climate change (Schubert et al., 2004).
Global warming  Precipitation shift from subtropics, greater evaporation, less snow/ice, and earlier spring  amplify the effects of natural climatic variations  intensified droughts and “dust-bowlification” (Romm, 2011).
(Source: Romm, Nature, 2011)

## Slide 29
Long-term Dust Trend
20 Giant Storms in 1990s  48 Storms in 2000s;

## Slide 30
Valley Fever (Coccidioidomycosis)
Infection caused by inhaling the soil-dwelling fungus Coccidioides
Coccidioidomycosis:
Lung infection;
Disseminated Coccidioidomycosis: Bloodstream transport to Skin, Brain, Nerve etc
(Source: thinklink.com)
2000 – 2011: 800% Increase in Infection;
3000 deaths caused by Valley Fever;
Notes: “San Joaquin Valley fever” or “desert rheumatism.” The term “Valley fever” usually refers to Coccidioides infection in the lungs, but the infection can spread to other parts of the body in severe cases (this is called “disseminated coccidioidomycosis”).

## Slide 31
Mysterious Spike in Valley Fever
800% Increase in Infection;
5,000 – 20,000 infections and 200 deaths each year;
Rates in the United States have increased dramatically
~10,000-20,000 cases reported to public health annually
>95% of cases are from Arizona and California
(Courtesy of Orion McCotter)

## Slide 32
Collocation of
Dust Storms and Valley Fever
(Tong et al., 2017)

## Slide 33
Highway Safety, Solar Power, Agriculture…
Highway traffic accidents caused by visibility loss and high wind
(Source: Giphy)
Dust deposition reduces power generation efficiency of solar farms
Notes: “San Joaquin Valley fever” or “desert rheumatism.” The term “Valley fever” usually refers to Coccidioides infection in the lungs, but the infection can spread to other parts of the body in severe cases (this is called “disseminated coccidioidomycosis”).

## Slide 34: On the day Americans file tax returns, there are always some big dust storms.
Tax-Day Dust Storms
(Tong and Tang, EM, 2018)

## Slide 35
CMAQ Dust Simulation with Baker-Schepanski Map
Surface PM10 during the Dust Storm

## Slide 36
Bring Science to Services
Support three dust services:
  Valley fever surveillance;
  Highway safety alert;
  Air quality management;
Use satellite-aided forecasts to:

## Slide 37
Dust Forecasting for Highway Safety
Highway dust forecasts:
Visibility
High Wind
Dust Concentration
Inhalable Particle Concentration
DustWatch App:
Citizen Scientist Project
Use dust forecasts
Real-time dust alerts
(Courtesy: Barry Baker)
(Contact Dust App. Team:
dustapp2018@gmail.com)

## Slide 38
CMAQ Lab: Wildfire Forecasting
Observations of the 2020 Gigafire;
https://www.star.nesdis.noaa.gov/smcd/spb/aq/AerosolWatch/
Install and Run the CMAQ model for the wildfire case;
https://docs.google.com/document/d/1_B4M4g4SqBTfdQFOb_vMq2ecPF-Z7Agw9YwFFzGRG4Y/edit?usp=sharing
3) Assignments:
  Read about the western fires this year, and write about 3-4 unique things about these fires.
  Finish running your CMAQ wildfire forecasting;
  Visualize your own results (hint: change this line in run_plot.sh): export aconc_dir="/home/cmaq/dtong/data/output"